## Slide 1: Low-Energy Adaptive Clustering Hierarchy An Energy-Efficient Communication Protocol for Wireless Micro-sensor Networks M. Aslam hayat

## Slide 2: Overview
Introduction
Radio Model
Existing Protocols
  Direct Transmission
  Minimum Transmission Energy
  Static Clustering
LEACH
Performance Comparison
Conclusions

## Slide 3: Introduction
LEACH (Low-Energy Adaptive Clustering Hierarchy) is a routing protocol for wireless sensor networks in which:
  The base station (sink) is fixed
  Sensor nodes are homogenous
LEACH conserves energy through:
  Aggregation
  Adaptive Clustering

## Slide 4: Radio Model

## Slide 5: Energy Analysis

## Slide 6: LEACH
In LEACH, the nodes organize themselves into local clusters, with one node acting as the local base station or cluster-head.
These cluster-head nodes broadcast their status to the other sensors in the network.
Each sensor node determines to which cluster it wants to belong by choosing the cluster-head that requires the minimum communication energy.
the cluster-head nodes are not ﬁxed.
The decision to become a cluster-head depends on the amount of energy left at the node.

## Slide 7: LEACH Algorithm
Advertisement Phase
Cluster Phase
Schedule Creation
Data Transmission
Hierarchical Clustering

## Slide 8: Advertisement Phase
For this “cluster-head-advertisement” phase, the cluster-heads use a CSMA MAC protocol, and all cluster-heads transmit their advertisement using the same transmit energy.
decideClusterHead {} in ns-leach.tcl

## Slide 9: Cluster Phase
After each node has decided to which cluster it belongs,it must inform the cluster-head node that it will be a member of the cluster.
findBestCluster{} and informClusterHead{}
Each node transmits this information back to the cluster-head again using a CSMA MAC protocol.
During this phase, all cluster-head nodes must keep their receivers on.

## Slide 10: Schedule Creation
The cluster-head node receives all the messages for nodes that would like to be included in the cluster.
Based on the number of nodes in the cluster, the cluster-head node creates a TDMA schedule telling each node when it can transmit.
createSchedule{}

## Slide 11: Data Transmission
Non-cluster-head send data during their allocated transmission time to the cluster-head.
The radio of each non-cluster-head node can be turned off until the node's allocated transmission time, thus minimizing energy dissipation in these nodes.
When all the data has been received, the cluster head node performs signal processing functions to compress the data into a single signal.
This composite signal is sent to the base station.

## Slide 12: Hierarchical Clustering
the cluster-head nodes would communicate with “super-cluster-head” nodes and so on until the top layer of the hierarchy, at which point the data would be sent to the base station.

## Slide 13: Radio Model
Designed around acceptable Eb/N0
Eelec = 50nJ/bit
  Energy dissipation for transmit and receive
εamp = 100pJ/bit/m2
  Energy dissipation for transmit amplifier
k = Packet size
d = Distance

## Slide 14: Radio Model

## Slide 15: Existing Routing Protocols
LEACH is compared against three other routing protocols:
  Direct-Transmission
    Single-hop
  Minimum-Transmission Energy
    Multi-hop
  Static Clustering
    Multi-hop

## Slide 16: Direct-Transmission
Each sensor node transmits directly to the sink, regardless of distance
Most efficient when there is a small coverage area and/or high receive cost

## Slide 17: Minimum Transmission Energy (MTE)
Traffic is routed through intermediate nodes
  Node chosen by transmit amplifier cost
  Receive cost often ignored
Most efficient when the average transmission distance is large and Eelec is low

## Slide 18: Energy Analysis of DT and MTE
direct communication energy equations
MTE communication energy equation
Simple linear network model

## Slide 19: Energy Analysis of DT and MTE
Simulation on mat lab using energy equation
100-node random network
2000 bit packets
εamp = 100pJ/bit/m2
High radio operation costs favor direct-transmission
Low transmit amplifier costs (i.e. distance to the sink) favor direct transmission
Small inter-node distances favor MTE

## Slide 20: LEACH: Operation
Periodic process
Three phases per round:
  Advertisement
    Election and membership
  Setup
    Schedule creation
  Steady-State
    Data transmission

## Slide 21: LEACH: Advertisement
Cluster head self-election
  Status advertised to nearby nodes
Non-cluster heads must listen to the medium
  Choose membership based on signal strength
    RSSI
    Eb/N0

## Slide 22: LEACH: Setup
Nodes broadcast membership status
  CSMA-CA
Cluster heads must listen to the medium
TDMA schedule created
  Dynamic number of time slots

## Slide 23: LEACH: Data Transmission
Nodes sleep until its time slots
Cluster heads must listen to each slot
Cluster heads aggregate/compress and transmit to Sink
Phase continues until the end of the round

## Slide 24: Low-Energy Adaptive Clustering Hierarchy (LEACH)
Adaptive Clustering
  Distributed
Randomized Rotation
  Biased to balance energy loss
Heads perform compression
  Also aggregation
In-cluster TDMA

## Slide 25: LEACH: Adaptive Clustering
Periodic independent self-election
  Probabilistic
CSMA CA used to advertise
Nodes select advertisement
with strongest signal strength
Dynamic TDMA time slots

## Slide 26: LEACH: Adaptive Clustering
Number of clusters determined
  Compression cost of 5nj/bit/2000-bit message
“Factor of 7 reduction in energy dissipation”
  Assumes compression is cheap relative to transmission
  Overhead costs ignored

## Slide 27: LEACH: Randomized Rotation
Cluster heads elected every round
  Recent cluster heads disqualified
  Optimal number not guaranteed
Residual energy considered
  P= Desired cluster head
  percentage
r = Current Round
G = Set of nodes which have not
  been cluster heads in 1/P
  rounds

## Slide 28: LEACH: Hierarchical Clustering
Not currently implemented
Efficient when network diameters are large

## Slide 29: Conclusions
LEACH is completely distributed
  No centralized control system
LEACH can reduce communication costs by up to 8x
LEACH keeps the first node alive for up to 8x longer and the last node by up to 3x longer